## Slide 1
The application of Finite Element Analysis in
Skeletal Biomechanics
2019
Mehdi Hassanzadeh
The University of
TEHRAN

## Slide 2
1/28
What is the application of Finite Element Analysis in Skeletal Biomechanics?
How accurate are the results?
How reproducible are the results?
A simple cantilever beam under shear force is discretized into a set of finite elements.

## Slide 3
2/28
Ref: Galea J.C. Analysing the microarchitecture of cribra orbitalia via... Diss. Master thesis, University of Bristol, 2013.
Bone adaptation
Optimal remodeling is responsible for bone health and strength throughout life.
Mechanical forces have a major contribution on the bone formation in both cortical and trabecular bone.
Imbalanced bone remodeling may cause bone mass reduction or osteoporosis.
Smart structure:
Stimulus
Sensor
operator

## Slide 4
3/28
Bone strength determined by:
The ability of bone against deformation (elastic modulus or stiffness)
Absorbing applied force/ energy (toughness)
Accommodating repetitive loading (fatigue strength)
Inhibition of progress of a crack (fracture toughness)
Ref: Brandi, Maria Luisa. "Microarchitecture, the key to bone quality." Rheumatology 48.suppl_4 (2009).
Bone Strength
Combination of:
Amount of bone present
The spatial distribution of the bone mass
The intrinsic properties of each of the bone components

## Slide 5
4/28
Normal mass and architecture
Loss of mass
deteriorated architecture
Bone Strength
Amount of bone present
The spatial distribution of the bone mass
The intrinsic properties of each of the bone components

## Slide 6
5/28
Ref: Kong,Deyin, et al. "Recent Advance in Evaluation Methods for Characterizing … (2019).
Mechanical test
Imaging modalities
FE Analysis

## Slide 7
6/28
Number (000)
BMD
Fx/1000 p-yrs
Women with Fxs
0
5
10
15
20
25
30
35
40
45
1
0.5 0
-0.5
-1
-1.5
-2
-2.5
-3
-3.5
0
100
200
300
400
Women
with Fxs
25%
57%
50
18%
60
70
80
age
50
- 1.0 SD
- 2.5 SD
75%
Fragility is not confined to women with osteoporosis
Ref: Siris et al Arch Intern Med. 2004;164(10):1108–12
Imaging modalities/DXA

## Slide 8
7/28
Ref: Zhao S, Arnold M, Ma S, et al. Standardizing compression testing for measuring…. Bone Joint Res. 2018
Philippe k Zysset et al. "Finite element analysis for prediction of bone strength." BoneKEy reports 2 (2013). //Video is created by researchers in ANU
Mechanical test
Obtaining the mechanical indices including; maximum load, ultimate strength, and maximum strain
Calculating the mechanical properties, such as the elastic modulus, energy absorption, and structural rigidity.

## Slide 9
8/28
Finite element analysis
Philippe k Zysset et al. "Finite element analysis for prediction of bone strength." BoneKEy reports 2 (2013).
Application of finite element (FE) analysis to determine stresses in human bones was initiated in the early 1970s in the field of orthopedic biomechanics.
In the 1990s, the availability of computed tomography (CT) provided feasibility of anatomical-specified FE modelling for selected parts or whole bones.
The development of computer hardware and software tools allowed substantial progress in the area of FE modelling validation and began the era of patient-specific FE modeling.
Finite Element Analysis (FEA) is a numerical and computerized method for predicting how a product reacts to real-world forces .

## Slide 10
9/28
FEA / Main concept
FEM, Useful for problems with complicated geometries, loadings, and material properties where analytical solutions can not be obtained.
1
2
3
4
5
Area?
Area=A1+A2-A3+A4+A5
Discretizing
Solving the problem for each parts
Assembling the results

## Slide 11
10/28
Many phenomena can be expressed by “governing equations” and “boundary conditions”
It is very difficult (maybe impossible) to solve these equations for the entire structure
Divide the domain into a number of small, simple elements
FEA / Main concept

## Slide 12
11/28
Governing Equation
(Differential equation)
L(φ ) + f = 0
B(φ ) + g = 0
Boundary Conditions
FE
You know all the equations, but
you cannot solve these eq. for the whole structure
FEA / Main concept

## Slide 13
12/28
2
3
5
1
5
4

## Slide 14
13/28
FEA / Outputs
The load-displacement curve can be achieved with FEA.
The linear part of the curve, i.e., stiffness, can be obtained with linear FEA, while the simulation of the yielding of the curve, the maximal force and the energy to failure requires nonlinear FEA.
Hart, Nicolas H., et al. "Mechanical basis of bone strength: influence of bone material..." Journal of musculoskeletal & neuronal interactions 17.3 (2017)
There are two behavioural characteristics either side of their yield point that are called as elastic and plastic regions.

## Slide 15
14/28
FEA / Accuracy
Ref: Zysset, Philippe K., et al. "Finite element analysis for prediction of bone strength." BoneKEy reports 2 (2013)
correlation coefficient

## Slide 16
15/28
FEA / Reproducibility
Reproducibility of the FEA results primarily depends on the reproducibility of the CT or other images on which the models are based.
Conditions | N | Reproducibility error | Reference
Short-term (1 week) Long-term (4 months) | 30 | Radius < 2.4 % Tibia < 3.6 % | MacNeil and Boyd (2008)
Short term Scanned three times | 15 | Radius < 2.3 % Tibia < 3.6 % | Ellouz et al. (2014)
The short-term and long-term reproducibility for multicenter studies using a radius phantom. | 14 (cadaveric distal radius bone) | Radius (multi-center )< 2.5 % | Burghardt et al. (2013)

## Slide 17
16/28
FEA / DXA
Group | N | micro-FE | DXA | Ref.
 | Fx Cases / Control | Δ strength % (control –Fx case) | UD radius aBMD % (control – Fx case) | 
Postmenopausal women | 33/33 | 15.3 | 13.9 | Boutroy et al. (2008)
Postmenopausal women | 100/105 | 20.2 | 11.9 | Christen et al.
Postmenopausal women | 14/28 | 46 | 12 | Nishiyama et al. (2013)
Postmenopausal women | 101/101 | 11.2 | 9.5 | Vilayphiou et al. (2010)
Postmenopausal women | 44/88 | 22 | 4 | Nishiyama et al. (2013)
Premenopausal women | 66/100 | 2.6 | 2.6 | Chevalley et al. (2013)
Men | 185/185 | 9 | 6.2 | Vilayphiou et al. (2011)
Van Rietbergen, B., and K. Ito. "A survey of micro-finite element analysis for clinical assessment of bone strength: the first decade." Journal of biomechanics 48.5 (2015).

## Slide 18
17/28
study
A novel pixel based image quantification analysis method
Numerical modeling of bone apparent density adaptation of the lower limbs in patients suffering from spinal cord injury

## Slide 19
18/28
An abrupt disruption to the bone metabolic process
Reduction of loads in lower limbs
Several mechanisms are responsible for this bone loss, but the removal of mechanical stimuli resulting from the loss of motor function and habitual ambulation is believed to be an important factor
study

## Slide 20
19/28
Bone loss process in SCI population
Regional bone loss may occur at rates approaching 1% of bone mineral density (BMD) per week at specific regional sites for the first several months after injury
Microgravity ( 0.25 % per week)
Bed rest ( 0.1 % per week)
Postmenopausal women are not taking anti-resorptive medications (3-5 % per year)
The Wolf’s law asserted that the bone structure would be adapted with the loading cycle which the bone experience
study

## Slide 21
20/28
Which kinds of rehabilitation activities?
How can we choose the effective rehabilitation method?
Are the effective rehabilitation methods different between each SCI patients?
Rehabilitation activities
study

## Slide 22
Clinical research in Rehabilitation Activities
Clinical researches are costly and time-consuming
Existence of different environmental variables which affect the final result especially for long term researches
The limitation at the length of the research
The limitation of data accusing from the volunteers due to the destructive effects of scanning methods
The Results aren’t patient specific
Using a FEM in order to reach a numerical model which can predict the bone structure, can provide the ability that different rehabilitation methods can be investigated for different time periods
21/28

## Slide 23
22/28
This procedure has been done by using the Mimics and Matlab software
A novel pixel based image quantification analysis method
Alignment and registration were performed separately for femur and tibia bones by creating four image stacks per scan
ROIs: epiphyseal (0–10 %) and metaphyseal (10–20 %) regions
1. A primary registration was done by using MIMICS registration function. This function allows registering two datasets by doing a landmark point-based registration.
2. A final registration was performed by using ICP FINITE registration program, an iterative closest point registration algorithm which is available in Matlab Central File Exchange.
study

## Slide 24
23/28
 |  |  | vBMD | Result % | 
Compact Bone |  |  |  |  | 
 |  |  |  | 1.812009383 | 
BMC | Result % | 
 | 4.96425588 | 
BV | Result % | 
 | 3.096144076 | 
study

## Slide 25
23/28
 |  | vBMD | Result % | 
Spongy Bone |  |  |  | 
 |  |  | 0.097747122 | 
BMC | Result % | 
 | 2.848288312 | 
BV | Result % | 
 | 2.948917916 | 
study
24/28

## Slide 26
Strain distribution
Max=1.846 mm
Max=1.768 mm
After the exercise
Before the exercise
25/28
study

## Slide 27
26/28
Numerical modeling of bone apparent density adaptation of the lower limbs in patients suffering from spinal cord injury
The main goal of this project is achieving an analytical and 3D model for prediction of bone loss in SCI patients (using FEA)
What's the application of the predictive model for SCI patients ?
What's the main purpose of this project?
study

## Slide 28
27/28
With this model, we can investigate all available rehabilitation methods to select more effective one based on patients’ level of injury
patient specific rehabilitation
What's the application of the predictive model for SCI patients ?
study

## Slide 29: Thanks for your attention
Mehdi Hassanzadeh
Mojtaba Haghighi-Yazdi
Morad Karimpour
Ali Ghasem-Zadeh
Gustavo Duque
Acknowledgments